## Slide 1
Stanislav Ondruš Zuzana Jelčicová

## Slide 2
+ Simple
+ Easy to implement
- Moving parts
- Prone to failure
Anemometer
Tipping bucket
Wind and rainfall measurements – existing solutions

## Slide 3: Wind and rainfall measurements – existing solutions
+ Maintenance free
- High cost
- Complex technology
Ultrasonic anemometer
Doppler radar

## Slide 4: Wind and rainfall measurements – our solution
IMU
F
Chart: Accelerometer [Z axis]

## Slide 5: Prototype

## Slide 6
Neural network
+ Powerful
- Memory and computationally demanding  increased energy dissipation  draining battery
Requirement
Weather station (ideally) functioning for months on a small battery
Solution
Smaller and simpler network (FC layers)
Hybrid solution
  Rain – neural network for rain classification
    Proof of concept - 4 types of rain (accelerometer):
      No rain
      Light rain
      Regular rain
      Heavy rain
    Model parameters: 31.6kB (8-bit data)
  Wind – speed and direction calculated using 2-channel strain gauge data  faster and cheaper

## Slide 7
Data collection, preprocessing and training
Rain simulation  dispersed water stream at different flow rates and intensities
3D-printed prototype of the weather station responsible for rain data collection
The IMU (LSM6DS3TR-C) interfaced through I2C on XIAO nRF52840
Continuous streaming of 3-channel accelerometer data (250Hz)
Data stream captured over serial port on a PC
Data divided into training and test subset (80:20)  Edge Impulse
Accuracy: 97.7%, Latency: < 25ms (Cortex-M4F 64MHz in nRF52840)
Heavy rain
Light rain
Regular rain
No rain

## Slide 8: Custom PCB
nRF52840
Battery powered
Low power
Development version
BLE Advertising

## Slide 9
Next steps
Sensing
Raindrop size and frequency - extracted from the accelerometer's AC content
Wind speed and direction - calculation based on strain gauge output
Hardware
Weather station assembly - material choice, shape optimization, DFM, etc.
Electronics - tests with the custom PCB

## Slide 10: Thank you!